## Slide 1: Tracker – Newton's Second Law
---以牛二運動為例
Tracker-6.1.3 版本
2023/9/8李芳瑜

## Slide 2: Download
Tracker Video Analysis and Modeling Tool for Physics Education (physlets.org) Tracker 免費影像分析軟體
: 請自行上網 download 適合自己電腦的版本
1. Tracker軟體是一個建立於Open Source Physics (OSP) Java 架構下的免費的影像分析與建模工具。
2. Tracker軟體可以由” Tracker Video Analysis and Modeling Tool for Physics Education (physlets.org) ”網頁下載。 適合的作業系統有Windows、MacOS 、Linux.
3.使用方式可參考 Tracker Help (physlets.org)

## Slide 3
Choose your Operating system to download

## Slide 4: Getting start
Open “Tracker”

## Slide 5: Language setting
Edit / Language /………
編輯 / 語言 /………

## Slide 6: Tracker --- menu bar

## Slide 7: How to start analyzing a video
Open a video or tracker file.
Identify the frames ("video clip") you wish to analyze.
Calibrate the video scale.
Set the reference frame origin and coordinate axis tilt.
Track objects of interest with the mouse.
Plot and analyze the tracks.
Save your work in a tracker file.
Export track data to a spreadsheet.
Print, save or copy/paste images for reports.
1.
2.
3.
4.
5.
7.

## Slide 8: 1. Open a video or tracker file
Method 1
Method 2
Method 3
File/ Open/File Chooser
File/Import/Video
Video/ Import
Tracker 可分析三種影片模式:
數位影片檔 (.mov, .avi, .mp4, .flv, .wmv, .ogg, etc.)
動畫檔 (.gif).
多個連續圖像 (.jpg, .png or pasted from the clipboard).
Tracker can analyze three different video types:
digital video files (.mov, .avi, .mp4, .flv, .wmv, .ogg, etc.) which require a video engine (see below).
animated GIF files (.gif).
images and image sequences consisting of one or more digital images (.jpg, .png, zip or pasted from the clipboard ).

## Slide 10: If need to rotate the video: Video filters
Video/ Filters/New/Rotate

## Slide 11: 2. Identify the frames ("video clip") you wish to analyze
frame
Play rate
step size
start and end frames
Select Zoom Level
Zoom in / zoom out:
Click on the film and roll the mouse wheel

## Slide 12: Video-Clip Settings (method 1) (設定取樣範圍與間隔)
Drag the black in- and out-point markers to set the start and end frames
Click the step size control to set the step size in frames per step.
start frame
step size (number of frames per step)
end frame

## Slide 13: Video-Clip Settings (method 2)
Tool bar / clip settings

## Slide 14: 3. Calibrate the video scale (設定比例尺)
1. calibration Stick : tool bar or Track/New/ calibration tool / calibration stick
1.
Tool bar “calibration tool” / New /Calibration Stick
Main bar “Track”/New/ calibration tool / calibration stick

## Slide 15: Calibration Stick
right-clicking on readout
Drag and nudge the ends of the stick to two points in the video that are a known real-world distance apart
Key in the reference data
right-clicking on Stick
V

## Slide 16: Unlocked calibration Stick
/Unlocked
/hide

## Slide 17: Units
Coordinate system/Units/

## Slide 18: 4. Set the reference frame origin and coordinate axis tilt- (設定坐標系)
Select and drag or nudge the origin
Select and drag or nudge the positive x-axis to rotate the axes
Show or hide coordinate axis

## Slide 19: Coordinate Axes
The pixel position of the origin and the angle of the +x-axis
Other axes settings

## Slide 20: 5. Track objects with the mouse - add track point
Track / New / Point Mass

## Slide 21: A. Manual tracking
1. shift-click once to mark a step at the mouse position,
2. or shift-enter to mark a step at the exact location of the previous step.
NOTE:
Don't skip frames
Zoom in for accuracy.

## Slide 22: A. Manual tracking-Delete
Delete 1 mark:
right-clicking the mark, choose “Delete”
Delete all mark:
choose “clear Steps”
Or
Track / Mass A
/ right-clicking,

## Slide 23: B. Auto tracking
Show or hide Autotracker
Or
Track / Mass A
/ autotracker…

## Slide 24: Select the target track (選擇追蹤參考點)
Shift-Ctrl-Click
使用快捷鍵 顯示質點設定，選取質點/自動追蹤軌跡
2. 設定範本: 在運動物體處 按Shift-Ctrl-Click 標記追蹤範本
(最好有明顯差異易追蹤之標記)

## Slide 25: Select the target track (選擇追蹤參考點)
Click “Search”
使用快捷鍵 顯示質點設定，選取質點/自動追蹤軌跡
2. 設定範本: 在運動物體處 按Shift-Ctrl-Click 標記追蹤範本
(最好有明顯差異易追蹤之標記)

## Slide 26: Click the Search button
hide
Show or hide the autotracker

## Slide 27: Auto track result
change the variable

## Slide 29: 7. Save your work in a tracker file
Tracker tab (.trk) :
Tracker saves the state of individual tabs (video clip, coordinate system, tracks and views)
Note that a Tracker tab file does NOT include the video itself, only a reference (relative path) to the video. If the video or Tracker tab file is moved separately then Tracker may not be able to find the video.
Tracker project (.trz) file :
A safer and better way to save a tab is in a Tracker project file (extension "trz") which DOES automatically include its own copy of the video along with a thumbnail image and HTML documentation. A project file opens in Tracker just like a tab file, but it's fully self-contained so you can move it and share it at will. Another advantage of project files is that you can browse and find
File / Save/ Project /

## Slide 30: Copy data (Use EXCEL Analyze)
Method 1:
Shift-dubble Click on table
Method 2:
Mouse Right Click : Copy Selected Cells
/ Full Precision

## Slide 31: Paste data in EXCEL
Or Ctrl-V
插入
At “A1”
Right-Click

## Slide 32: Export data
Text Files (.txt)
File / Export / Data
/ Save as

## Slide 33: Analyze---Use tracker
Or Dubble Click on plot
 Data tool
access display and analysis options in a popup menu
Right-Click on a plot
Right-Click on a table

## Slide 34: Data tool
Plot or not

## Slide 35: Newton‘s Second Law (2次函數)
Analysis / Curve Fitter / Cube (三次式)
用3次式改2次式

## Slide 36: Newton‘s Second Law (2次函數)
X=-0.1016t2-0.141t+0.00658
vs. x=v0t+1/2at2
a=0.2032 m/s2
可更改起始參數
用3次式改2次式

## Slide 37: Set new Fit Function Newton‘s Second Law (2次函數)
Fit Builder
Dubble Click
X=0.5*(-0.203)*t2-0.141t+0.007